## Slide 1: Computer Architecture
Instructions

## Slide 2: Hierarchy of Computer Languages

## Slide 3: Instruction Codes
Program
  A program is a set of instructions that specify the operations, operands and the sequence by which processing has to occur.
Computer Instruction
  A computer instruction is a binary code that specifies a sequence of micro-operations for the computer.
  The computer reads each instruction from memory and places it in a control register.
  The control then interprets the binary code of the instruction and proceeds to execute it by issuing a sequence of micro-operations.
Instruction Code
  An instruction code is a group of bits that instruct the computer to perform a specific operation.
  Example
Operation Code (Opcode)
  The operation code of an instruction is a group of bits that define such operations as add, subtract, multiply, shift, and complement.
  The number of bits required for the operation code of an instruction depends on the total number of operations available in the computer.
  The operation code must consist of at least n bits for a given 2n (or less) distinct operations.
ADD 1547
Unique Binary code is assigned to every Opcode

## Slide 4: Stored Program Organization
Operand
(data)
Instructions
(program)
Memory
4096 x 16
Processor Register (accumulator or AC)
Opcode
Address
0
11
12
15
Instruction Format
Binary Operand
0
15
Opcode: Specifies the type of operation to be performed.
Operand: Provides information on the data needed for the instruction execution.

## Slide 5: Stored Program Organization
The simplest way to organize a computer is to have one processor register(AC) and an instruction code format with two parts.
  The first part specifies the operation (opcode) to be performed and the second specifies an address (operand).
The memory address tells the control where to find an operand in memory.
This operand is read from memory and used as the data to be operated on together with the data stored in the processor register.
Instructions are stored in one section of memory and data in another.
For a memory unit with 4096 words, we need 12 bits to specify an address since 212 = 4096.
If we store each instruction code in one 16-bit memory word, we have available four bits for operation code (opcode) to specify one out of 16 possible operations, and 12 bits to specify the address of an operand.
The control reads a 16-bit instruction from the program portion of memory.
It then executes the operation specified by the operation code.

## Slide 6
Instruction: The words of a computer language is called instruction
Instruction set : The vocabulary of computer language is called instruction set.
Goal of the computer designer:
To find a language that makes it easy to build the hardware and compiler while maximizing performance and minimizing cost.

## Slide 7: Instruction Set Classification

## Slide 8
Data Movement Instructions: These support movement of data between registers, registers to memory, memory to register.
Arithmetic and Logical Instructions: This category of instructions carry out calculations. The minimum in this category is ADD, SUB, AND, OR, XOR, SHIFT. Multiply and Divide can always be emulated using successive addition or subtraction.
Transfer or Control Instructions: This category of instructions facilitate change in program flow described by the control structures in the high-level language. BRANCH or JMP instructions along with Condition Code flags achieve the requirement. Subroutine CALLS, RETURNS are categorized here.

## Slide 9
Input/Output Instructions: There are two ways of doing Input/Output operations.
Miscellaneous Instructions: NOP (No Operation) is a famous dummy instruction but a very useful one in this category.
Floating Point Instructions: We had seen in the previous chapter that specialised hardware is required for efficient Floating-point operations.
Binary Coded Decimal Instructions: Decimal Number system hardware speeds up decimal calculations.

## Slide 10
CPU architecture design radically differs based on the size of the Instruction set. Accordingly, there are two categories namely Reduced Instruction Set Computer (RISC) and Complex Instruction Set Computer (CISC). As the name implies, RISC has

## Slide 11
Instruction Formats and Classification
The components to be considered while deciding and designing instruction format is:
The number of instructions in the instruction set
The number of CPU registers to be addressed
Size of Main memory to be addressed and organization
Addressing modes to be mapped
Encoding of Instructions is called Instruction Format. There are two generic ways to encode instructions.
Fixed length Instruction Format - RISC uses fixed-length encoding.
Variable Length Instruction Format - CISC uses variable-length encoding.

## Slide 12
Each instruction occupies only the space required by it to convey the operands. No redundant use of memory space.
Essentially this format provides more options to address more operands.
Calculating the next instruction location is complex and depends on the current instruction type.
The fetch and decode logic and Control Unit design is complex.
Code efficiency is possible, but frequent memory reference implies relatively reduced efficiency.
A Large number of instructions have different opcodes but same function, implying varying addressing modes.
Each Instruction occupies the same amount of space. The length of the instruction is fixed irrespective of the opcode.
The instruction fetch process is simpler. The next instruction address is obtained by incrementing the Program Counter by a fixed count.
The instruction decoding process is also simpler and hence the Control Unit design is less complex comparing variable-length format.
Faster and better performance, as the design, makes use of CPU Registers more effectively.
The program code (machine code) for these machines is longer and proportional to the number of instructions.
Few simple instructions equivalent to HALT, NOP which do not require any operand also occupies the same length and size of memory. A little waste of memory space at the cost of CPU efficiency.
Variable Length Instruction format
Fixed Length Instruction format

## Slide 13
Variable Length Instruction format

## Slide 14
Fixed Length Instruction format

## Slide 15
Operations of the computer hardware:
--per line one instruction
--must always have exactly three variables
MIPS (an acronym for Microprocessor without Interlocked Pipeline Stages) is a reduced instruction set computer (RISC) instruction set architecture (ISA) developed by MIPS Technologies (formerly MIPS Computer Systems)

## Slide 16
Operands of the computer hardware:

## Slide 17
Answer:

## Slide 18
How computer hardware access large memory structure?
--- Data structures (array and structures) are used.
Data transfer instruction:
A command that moves data between memory and register
Memory to register = load
Register to memory = store

## Slide 19
g=h + A[8]
Answer:
lw $t0, 8($s3) offset
base register
add $s1, $s2, $t0

## Slide 20
Alignment register:
Words must start at address that are multiples of 4.
Spilling register:
Process of putting less commonly used variable in a memory is called spilling register.

## Slide 22: Representing Instructions in the computer:

## Slide 23
R-type:

## Slide 24
Example:
add $t0, $s1, $s2
op = 0
rd= $t0 = 8
rs= $s1 = 17
rt= $s2 = 18
Shmt = 0
Funct = 32
0 | 17 | 18 | 8 | 0 | 32
000000 | 10001 | 10010 | 0100 | 000000 | 100000

## Slide 25
I – format :
Example:
lw $t0, 32($s1)
j- type:
Opcode=2
Address=given address/4;
35 | 17 | 8 | 32

## Slide 27: Decision making statement:

## Slide 28
if ( i==j) go to L1;
f = g+h;
L1: f=f-i;
Convert this into MIPS assembly code.
Answer :
f= $s0, g= $s1, h= $s2, i= $s3, j= $s4
beq $s3, $s4, L1
add $s0, $s1, $s2
L1: sub $s0, $s0, $s3

## Slide 29
Answer:
bnq $s3, $s4, ELSE
add $s0, $s1, $s2
j EXIT
ELSE:
sub $s0, $s1, $s2
EXIT
N.B: use jump in case of if… else

## Slide 30
Loop: g= g + A[i]
i=i+j
If (i!=h) go to LOOP.
What will be the MIPS assemble code?
Answer:
g=$s1, h=$s2, i=$s3, j=$s4, A=$s5
Loop:
add $t1, $s3, $s3
add $t1, $t1, $t1
add $t1, $t1, $s5 // $t1= address of A[i] (4*i + $s3)
lw $t0, 0($t1) // used that address to load A[i] into a temporary register
add $s1, $s1, $s4
add $s3, $s3, $s4
bne $s3, $s4, LOOP
Rule for getting address of an array:
1.Multiply the index I by 4
2. Add with the base of array

## Slide 31
while (save [i] = k )
i= i+j
what will be the MIPS assembly code for this?
Answer:
i=$s3, j=$s4, k=$s5, save = $s6
LOOP:
add $t1, $s3, $s3
add $t1, $t1, $t1
add $t1, $t1, $s6
lw $t0, 0($t1)
bne $t0, $s5, EXIT
add $s3, $s3, $s4
j LOOP
EXIT

## Slide 33
What is the code to test if variable a (=$s0) is less than variable b (=$s1) and then branch to label LESS if the condition holds?
Answer:
slt $t0, $s0, $s1
bne $t0, $zero, LESS
If $s0 < $s1
$t0=1
If $s0 > $s1
$t0=0

## Slide 38
Register Addressing:
Register Addressing is a source or destination operand is specified as content of one of the registers.
Register Addressing is considered the simplest addressing mode. This is because both operands are in a register.
Which allow instructions to be executed much more faster in comparison with other addressing modes because they does not involves with memory access.
The number of registers is limited since only a few bits are reserved to select a register.
Register Addressing is a form of direct addressing , this is because we are only interested in the number in the register , rather than using that number as a memory address.
Here's an example of Register Addressing : add $s1 , $s2 , $s3 also means that $s1 ←$s2 + $s3
where ; $s1 = rd
$s2 = rs
$s3 = rt

## Slide 39
Immediate Addressing:
Immediate Addressing is a numeric value embedded in the instruction in the actual operand.
In immediate addressing , the operand is a constant within the encoded instruction.
Immediate addressing has the advantage of not requiring an extra memory access to fetch the operand , hence will be executed faster. However , the size of operand is limited to 16 bits.
The jump instruction format also falls under immediate addressing , where the destination is held in the instruction.
Now an example of Immediate Addressing :
addi $t1 , $zero , 1 means $t1 ← 0 + 1
(add immediate , uses the I-type format)
where ; $t1 = rd
$zero = r1
1 = immediate value

## Slide 40
Base Addressing:
Base Addressing is a data or instruction memory location is specified as a signed offset from a register.
Base addressing is also known as indirect addressing , where a register act as a pointer to an operand located at the memory location whose address is in the register.
The register is called base that may point to a structure or some other collection of data and immediate value is loaded at a constant offset from the beginning of the structure. The offset specifies how far the location of the operand data from the memory location pointed by the base.
The address of the operand is the sum of the offset value and the base value(rsHere's an example for Base Addressing :
Instruction : lw $t1 , 4 ($t2)
where $t1 = rs
$t2 = base (memory address)
4 = offset value
Thus ; $t1 = Memory [$t2 +4]

## Slide 41
PC-Relative Addressing:
PC-Relative Addressing also known as Program Counter Addressing is a data or instruction memory location is specified as an offset relative to the incremented PC.
PC-relative addressing is usually used in conditional branches. PC refers to special purpose register , Program Counter that stores the address of next instruction to be fetched.
The effective address is the sum of the Program Counter and offset value in the instruction. The effective address determines the branch target.
In PC-relative addressing , the offset value can be an immediate value or an interpreted label value.
Another word of saying to explain PC-Relative Addressing :
The operand address = PC + an offset

## Slide 42
Pseudo-direct Addressing:
Pseudo-direct Addressing is the memory address which (mostly) embedded in the instructions.
Pseudo-Direct addressing is specifically used for J-type instructions. The instruction format is 6 bits of opcode and 26 bits for the immediate value (target).
In Pseudo-Direct addressing , the effective address is calculated by taking the upper 4 bits of the Program Counter(PC) , concatenated to the 26 bit immediate value , and the lower two bits are 00.